## Slide 1
After improvement
Breakthrough
Before improvement
Index validation in GantryForm to prevent crashes
Install PCB - vendor software AlphaRap-SRM 1.1.0.18
PHENOMENON
IMPROVEMENTS
The piece in position 12 was never registered as processed, so the pallet travelled all the way to the Unloader before being released. Sporadic 50014 unhandled-exception alarms also appeared, with no line or method in the log.
EFFECT:
Pallets with an unregistered piece in position 12 went from practically every pallet to none during the validation shift. All changes tagged MOD@@ Guillermo Carrillo in the source code.
DX Level 구분 |  | 
A2D | 정보화 | 지능화
개선 영역 | Analog BP | DX BP
이물/생산성 |  | 
성능/품질 | ○ | 
프로세스 |  | 
안전환경 |  | 
고객가치 |  | 
전파 | 광학 | 기판 | 전장 | CTO | 전자 | 생기 | 품질
 | ○ | △ | △ | △ | △ | X | X
PROBLEM
21 index guards added to GantryForm.cs, covering arrays and lists, including the four on palletResultCopy that caused the position-12 failure.
The vendor accesses arrays and lists without validating bounds. On the last piece of the pallet the index falls out of range and the exception aborts the flowchart node before the piece is reported.
The 1211 "Cover is tilted" alarm is raised from a single camera reading, so capture noise is read as a real tilted cover.
■ Date : 18/09/2026 ■ Writer : Guillermo Carrillo ■ Division: CM ■ Team: Production Engineering
IMPACT:
No more pallets reaching the Unloader with an unregistered piece.
1211 alarms: baseline 24-36 per 12 h shift. New figure pending measurement.
The guards are portable to the rest of the stations without modifying their flowcharts.
Retry dialog added on QR read failure (alarm 1302), so the operator can reposition the PCBs instead of losing the group.
1211 alarm now confirmed by voting: 5 readings 150 ms apart, alarm raised only when 3 or more agree. Threshold configurable and recorded in the log.